## Slide 1
TRAINING · SOURCE-ARCHIVE DEEP DIVE
NORD Time Sharing System
An introduction to TSS by Bo Lewendal — kernel, user space, and every device down to the register bits — ending at the deepest layer: the NORD-10 swapping-drum driver.
TSS1–TSS5 · MAC ASSEMBLER
NORD-1 / NORD-10
DRUM DRIVER: NJL · 17 APR 1973
Notes: This training covers the recovered NORD TSS source archive end to end: the OS, its architecture and subsystems, every I/O device with registers and bits, a deep dive on the swapping drum, and how to build, install and run it.

## Slide 2
INTRODUCTION
What TSS Is
01
A complete, standalone timesharing operating system for the NORD-1 and NORD-10. It owns the machine — it is not a program running under SINTRAN.
02
Written by Bo Lewendal in MAC assembler, in five source parts, with the algorithms documented in structured pseudo-code comments beside the code.
03
Every terminal is a process with its own 8-page virtual memory, swapped between core and mass storage — CDC disk, or a drum.
04
Users get a command processor, a file system, mail, accounting — and programs get a monitor-call interface.
5
source parts, TSS1–TSS5
≈14,000
lines of MAC assembler
81
monitor calls in MCTBL
24
teletypes maximum
Notes: TSS is not a program under SINTRAN. It IS the operating system - it owns the whole machine. Five parts of MAC assembler, about 14,000 lines, one process per terminal.

## Slide 3
INTRODUCTION
The Source Archive
FILE
CONTENTS
LINES
TSS1:SYMB
Kernel — interrupts, all device drivers, scheduler, swapper, page tables
4,709
TSS2:SYMB
Context block, monitor-call implementations, command processor
3,512
TSS3:SYMB
Overlay machinery (GOVER / OVERL / OVERX) and system utilities
1,755
TSS4:SYMB
Utility overlays — DUMP, RECV and friends
2,040
TSS5:SYMB
User-management overlays — create / delete user, accounts
1,995
ASSYSA / ASSYSB
MAC build scripts — version A, and version B with DEBUG mark
25 ea.
MINIT / TDUMP
Standalone mass-storage initializer and TSS dumper
810 / 383
The archive also holds the build outputs : LIST1–LIST5 listing streams, plus ASYMB / BSYMB — complete symbol-table dumps that serve as a golden oracle for any re-assembly.
Notes: The archive splits into source and build output. LIST and ASYMB files prove the build scripts were run through a real MAC assembler - and ASYMB/BSYMB give a golden symbol table to verify any re-assembly against.

## Slide 4
INTRODUCTION
The Big Picture
USERS
Up to 24 teletypes
one logged-on user → one process
USER SPACE · S02
8 × 2K pages @ 40000₈
command processor · utility overlays · user programs — swapped
KERNEL · S01
Resident TSS
scheduler · swapper · monitor calls · buffers · file system · drivers
DEVICES · S03
TTY · tape · cards · printer · CDC disk
registers & bits, via IOT / IOX
THE DRUM · S04
XDRUM @ IOX 540₈
the swap device — full register & bit walkthrough
BUILD & RUN · S05
FMAC + ASSYSA
marks → assemble → save to disk → boot standalone
Notes: One mental model for the whole course. Users on teletypes talk to a per-process world above 40000 octal. The resident kernel below is driven by the interrupt-level system, and everything lands on the devices. Sections: 01 kernel, 02 user space, 03 devices, 04 drum, 05 build and run.

## Slide 5
01
The Kernel
Resident TSS: interrupt levels, memory management, scheduler, swapper, monitor calls, buffers, and the file system.
Notes: Section one: the resident kernel - interrupt architecture, memory management, scheduling, swapping, monitor calls, buffers and the file system.

## Slide 6
SECTION 01 · KERNEL
Interrupt-Level Architecture (NORD-10 build)
14
Traps — illegal instruction, protect violation, monitor-call decode
6
Teletype scanner — polls dead terminals every 80 ms
13
Real-time clock
5
Scheduler + swapper (LEV5 → SWAPR)
12
Input interrupts — TTY in, reader, cards (IDENT PL12)
3
Monitor-call processor — dispatch through MCTBL
11
DMA devices — Versatec printer option
2
Utility level — command processor entry, user services
10
Output interrupts — TTY out, punch, line printer
0
Idle loop — traps WAIT, hands control onward
9
Subsidiary clock — quanta, timeouts, response timers
NORD-1 build: levels 7 / 11 and IOT instructions instead
False interrupts and I/O errors are counted per level in NER10 / NER11 / NER12 / SER10 / SER12 / SER23 / NIOX cells — built-in diagnostics for flaky hardware.
Notes: On the NORD-10 every kernel component runs on its own hardware priority level. Level 5 holds both scheduler and swapper. Levels 10, 11, 12 are device levels; 14 catches traps and dispatches monitor calls to level 3. The NORD-1 build uses levels 7 and 11 with IOT instead.

## Slide 7
SECTION 01 · KERNEL
Memory Management
VCTBL
Virtual core table — the 8 pages the current process wants : mode, swap index, disk address.
PCTBL
Physical core table — what actually sits in each of the 8 core page frames right now.
PDTBL
“Physical drum table” — the swap-space allocator: usage count, mode, file address per swap page.
Page modes drive swap policy: MD=1 scratch (never written back), MD=2 read-only — shared between processes via a reference count in PDTBL, MD=3 read/write (written out on every switch).
User space: NPGS=8 pages of 2K words at MSTRT=40000₈ . Swap pool: 36–72 pages, scaled by the TEL n mark.
SMPR rebuilds protection after every switch: memory-protect registers on the NORD-1 (2K / 4K blocks) — real paging registers at 177400₈ on the NORD-10 (IPGTB sets them up at boot).
A process's registers live in its context block (RBLOK), stored as swap page 0 — 8 sectors at DKA1 + index×8.
Notes: Three tables run the memory system. VCTBL is what the process wants, PCTBL what is in core, PDTBL what is on swap. Modes: 1 scratch, 2 read-only shared with reference counting, 3 read-write. SMPR rebuilds protect or paging registers after each switch.

## Slide 8
SECTION 01 · KERNEL
Scheduling
% PROCESS TABLE (PRT) — 8 WORDS / PROCESS
PRT1, 0 %PDTBL INDEX OF CONTEXT BLOCK
0 %QUANTUM TIMER
0;0 %COMPUTE TIMER
0 %STATUS: BLOCK·RUBOUT·I/O BITS
0 %TTY USAGE (<0 DEAD, 0 INIT, >0 ALIVE)
0 %FREE WORD
0 %SAVED PID
QUANT, -17 %QUANTUM (NEG. TICK COUNT)
LQUA, 24 %SMALL QUANTA PER LARGE QUANTUM
The subsidiary clock (level 9) increments the running process's quantum timer each tick and wakes level 5.
LEV5 scans PRT round-robin . The incumbent keeps core until it blocks, dies, or burns LQUA small quanta; then the next runnable process wins.
A context switch is a call to SWAPR — scheduling and swapping are one mechanism, because switching processes means swapping memory.
Notes: PRT is the process table, eight words per terminal. The clock on level 9 counts quanta; level 5 scans PRT round-robin. Exhausting the large quantum, blocking, or dying triggers SWAPR with the successor.

## Slide 9
SECTION 01 · KERNEL
Swapping — SWAPR
1
Write the outgoing process's context block: TRSFR(WRITE, @RBLOK, DKA1+(PRT[0]<<3))
2
Read the incoming process's context block, restore its registers
3
For each of 8 pages: write out conflicting read/write pages (MD=3), keep matching ones, delete abandoned ones
4
Read in required pages — a shared read-only page already in the pool is reused by bumping PDTBL[j]$COUNT, never copied
5
Every transfer goes through one routine: TRSFR — 2K words between core and swap space. That routine is where the drum plugs in (S04).
Notes: SWAPR's five steps. This is where TRSFR appears - the routine the drum section dives into. Note the sharing logic: a read-only page already in the swap pool is reused by bumping its reference count, not copied.

## Slide 10
SECTION 01 · KERNEL
Monitor Calls
A user program executes a monitor-call opcode → trap on level 14 → the call number indexes MCTBL → the handler runs on level 3 with the user's registers.
Three return styles: normal, skip return (success/failure), and double-skip — the caller places its error handling right after the call, like the device drivers do.
Level 14 also emulates missing hardware : LBYTE, SBYTE, register multiply / divide, EXRG — so one binary runs on differently-equipped machines.
% MCTBL — 81 ENTRIES, BY THEME
CHAR I/O INBT OUTBT ECHOM BRKM
FILES OPEN CFILE ISIZE OSIZE
DISK RDISK WDISK RPAG WPAG
STRINGS SETUP GCI WCI TRIM CNS
USERS GUNUM GUNAM WHUSR EXEC
MAIL IMAIL GMAIL BROAD MSG
TIME RKLOK RDATE TTIM RCTIM
CONTROL LEAVE RESUM ESCTR DBRK
Notes: Programs reach the kernel through monitor calls: trap on level 14, decode, dispatch on level 3 through MCTBL, 81 entries. Level 14 also emulates instructions the machine lacks: byte load and store, register multiply and divide.

## Slide 11
SECTION 01 · KERNEL
Buffers & the Driver Pattern
Every character device owns a ring buffer (two 8-bit chars per 16-bit word), created by IBUF and reached only through WBUF / RBUF.
Drivers split in two halves that meet in the buffer: an interrupt half on the device level (TTYDI, READR, CARD1, PNTDR…) and a process half called via monitor calls (RTTY, WTTY, RREA, WPRNT…).
Skip-return convention : a routine returns to the instruction after the call on failure, skips one on success — callers write their error handling in line, no flags.
A busy flag per buffer marks a transfer in flight; a full output buffer blocks the process (PRT status bit) until the drain interrupt wakes it.
% OUTPUT PATH, e.g. WTTY
PROCESS: WTTY → BUSY?
NO → IOX WDR (START DEVICE)
YES → WBUF (QUEUE CHAR)
FULL → BLOCK PROCESS
% INTERRUPT (LEVEL 10)
TTYDO: RBUF → IOX WDR
EMPTY → BUSZR, UNBLOCK
% INPUT MIRRORS IT ON LEVEL 12
TTYDI: IOX RDR → WBUF → BRKCH
Notes: The kernel's driver pattern. Every character device owns a ring buffer packing two characters per word, described by a BUFTB descriptor. Drivers come in interrupt halves - TTYDI, READR, CARD1, PNTDR on the device levels - and process-side halves - RTTY, WTTY, RREA, WPRNT - that meet in the buffer. Skip-return exits encode success and failure. Busy flags plus device locks serialize everything.

## Slide 12
SECTION 01 · KERNEL
The File System
Storage past FSYS is allocated in tracks through a bit table ( BITBL, 400₈ words) in the master information block — GTRK grabs a track, RTRK returns it.
The user table (USTBL) maps users to their file directories; OBT tracks up to NOPEN=16 open files (64 words of state each).
Every file-system transfer moves 2K words through TRXX → the CDC disk driver — the same size as a swap page.
% DEFAULT FILE TYPES
'BIN' BINARY 'PROG' DUMPS
'BRF' RELOC. 'SYMB' SOURCE
'DATA' DATA 'CORE' SAVES
'RB' RB FILES
In-core caches with lock words: BITBL / USTBL / BTEMP each carry LOCK · IN-CORE FLAG · DEVICE ID headers — one 256-word disk sector cached at a time.
Notes: The file system lives past the swap areas. A master information block with a bit table allocates 256-word tracks; the user table maps 8 users per device; OBT holds up to 16 open files. Files are typed by name suffix. All file-system transfers are 2K reads and writes through TRXX.

## Slide 13
02
User Space
Command processor, utility overlays, and user programs — the swapped world above 40000₈.
Notes: Section two: what runs above 40000 octal - the command processor, the overlay utilities, and user programs.

## Slide 14
SECTION 02 · USER SPACE
Logon & the Command Processor
A keypress on a dead terminal wakes the level-6 scanner → the scheduler initializes the process → SWAPR's cold path ( S10 ) acquires a context block, sets logon mode , and loads the command processor from the coreload area (CORL1 / CORL2).
Commands parse through the string machinery (CMDLN , GCMD, PCF) and either run in-line or pull a utility overlay.
RUBOUT / ESC is sacred: it fires the break logic, RSLK releases every lock, and the utility restarts — the guaranteed way out of anything.
% PER-PROCESS STATE (TSS2)
CMDLN COMMAND LINE BUFFER
RUBAD ESCAPE TRAP ADDRESS
RUBPR SAVED P AT RUBOUT
RMODE 0 NORMAL / -1 LOGON
OVLAY CURRENT USER OVERLAY
PRNUM PROJECT NUMBER
TSS measures itself: RSTIM / RSNUM accumulate response time per break character — 1970s telemetry.
Notes: Logon: a keypress on a dead terminal wakes the scanner, SWAPR builds a fresh process with the SINIT or LEV2 entry, and the command processor is read from the coreload area. Rubout - ESC - always returns control: RSLK clears all locks and the utility restarts. The response-time counters measure it.

## Slide 15
SECTION 02 · USER SPACE
Utility Overlays & User Programs
Utilities live as 1000₈-word overlays in OVDK on disk. Calling one is a macro: GOVER traps to the loader, which swaps the overlay into the ROVER window and jumps in.
The build trick: OVERX writes each overlay to disk while MAC is still assembling — assembly and installation are the same act.
TSS4/TSS5 overlays: DUMP · RECV · CRUSE · DLUSR · account and mailbox maintenance.
% USER PROGRAM LIFE CYCLE
RECV 'PROG' FILE → PAGES+REGS
RUN SWAPPED LIKE ANY PROCESS
MON CALLS INTO MCTBL
DUMP PAGES+REGS → 'PROG' FILE
DUMP stores the full machine state — registers, RUBAD, a magic word 131313₈ — so RECV resumes a program exactly where it stopped.
Notes: User-space code beyond the resident command processor comes in as overlays: GOVER traps to the overlay loader, which reads 1000-word overlays from OVDK. The wild part: OVERX writes each assembled overlay to disk during assembly. User programs are saved and restored as PROG files by DUMP and RECV with full context.

## Slide 16
03
The Devices
IOT and IOX at the bit level — then terminal, tape, cards, printer and CDC disk, register by register.
Notes: Section three: the device complement - the I/O instructions themselves, then every peripheral with its registers and bits.

## Slide 17
SECTION 03 · DEVICES
Talking to Hardware: IOT and IOX
"NN10 — NORD-1 · IOT = 160000₈ + bits
15–13 OPCODE 7₈
11 PIN 2000₈
9 SKA 1000₈
8 ACT 400₈
7–0 DEVICE NO.
ACT ACTIVATE / TRANSFER DATA
SKA SKIP NEXT IF DEVICE READY
PIN PERMIT (ENABLE) INTERRUPT
SNI SKIP IF NO INTERRUPT (SCAN)
IOT ACT REA % READ TAPE CHAR → A
IOT PIN ACT DFP % PUNCH A + INT
"N10 — NORD-10 · IOX / IOXT
15–11 OPCODE
10–1 · DEVICE REG. ADDRESS
0 · R/W EVEN/ODD
EVEN ADDR → DEVICE READS INTO A
ODD ADDR → A WRITTEN TO DEVICE
IOX REA RDR % 400 → READ CHAR
SAA 5; IOX DCR WCR % 423 ← CONTROL
IDENT PL12 % WHO INTERRUPTED?
IOXT: REG. ADDRESS TAKEN FROM T
→ FULL 0–177777₈ ADDRESS RANGE
Every TSS driver is written twice inside "NN10 / "N10 conditional blocks — one source, two machines. TSS uses plain IOX throughout; device numbers stay below 2000₈.
Notes: How the CPU physically talks to hardware. NORD-1: one IOT instruction, opcode 160000 octal, device number in the low bits, function bits ACT SKA PIN SNI ORed in. NORD-10: IOX, low 11 bits are a device-register address - even reads into A, odd writes from A. IOXT takes the address from T for the full 16-bit range. Every driver exists twice under NN10 and N10 marks.

## Slide 18
SECTION 03 · DEVICES
The Standard Device: 4 Registers (NORD-10, base + 0…3)
+0 RDR
read data → A
+1 WDR
write data ← A
+2 RSR
read status → A
+3 WCR
write control ← A
% CONTROL VALUES IN TSS
5 = INT + ACTIVATE (TTY,TAPE,LP)
7 = INT + ERR-INT + ACT (CARDS)
3 = INTS ONLY, NO ACTIVATE
20 = DEVICE CLEAR (ERROR RECOVERY)
0 = DISARM (QUIESCE DEVICE)
STATUS REGISTER (RSR) — BITS AS TESTED BY TSS
bit 0
interrupt enabled (readback of WCR bit 0)
bit 3
device ready for transfer — polled as BSKP ONE 30 DA
bit 4
inclusive OR of errors — BSKP ZRO 40 DA guards every driver
bit 5+
device-specific (framing / parity / card-done …)
CONTROL REGISTER (WCR)
4 DEV.CLEAR
3 TEST
2 ACTIVATE
1 INT ON ERR
0 INT ON RDY
Bit numbers in ND notation: BSKP … 30 DA = bit 3, 40 = bit 4, 170 = bit 15 (octal tens = bit index).
Notes: The NORD-10 standard device: four registers. Status and control bits follow one convention across all character devices - these exact bits are what the TSS drivers test. Control values you will see everywhere: 5 to arm and run, 7 on the card reader, 20 octal device clear on the printer, 0 to disarm.

## Slide 19
SECTION 03 · DEVICES · TTY
Terminals IOX 300₈+10₈n · in = base, out = base+4
300 / 304
TTY1 read data / write data
302 / 306
TTY1 read status (in) / (out)
303 / 307
TTY1 write control (in) / (out)
…1370
TTY9–16 at 1300–1370
STATUS BITS USED (RSR)
bit 3
char received / transmitter ready
bit 4
error OR → counted in SER10/12/23
WCR←5
arm interrupt + activate after each char
% INPUT FLOW (TTYDI, LEVEL 12)
IOX ttyi RSR → BIT 4 SET? → TERR
IOX ttyi RDR → CHAR → CKPAR PARITY
WBUF: RING BUFFER, 2 CHARS/WORD
BRKCH: BREAK STRATEGY 0/1/2/USER
ECHCH: ECHO NOW / DEFERRED / NONE
IOX ttyi WCR ← 5 (REARM)
Break decides which character wakes the process; echo can run at interrupt level (full duplex) or be deferred into an echo buffer so program output stays coherent. Buffer descriptors carry both tables per terminal (words 11–30 of each BUFTB entry).
Notes: The terminal, the most elaborate driver. Base 300 plus 10 octal per unit; input at base, output at base plus 4. The driver flow: interrupt, read status, check error bit 4, read the character, parity check, into the ring buffer, break and echo strategy. The scanner on level 6 revives logged-out terminals.

## Slide 20
SECTION 03 · DEVICES · TAPE + CARDS
Paper Tape & Card Reader
TAPE READER 400₈ · PUNCH 410₈
400 RDR
read tape character → A
402 RSR
bit 3 char ready · bit 4 error
403 WCR
← 5 read next char + interrupt
411 WDR
punch character ← A, then WCR←5
A stuck reader is released by the 5-second timeout (TIMOUT=-372₈ ticks) on the clock level; buffers: 9PPT=600₈ in, 9FP=600₈ out.
CARD READER 420₈
420 RDR
read column code → A
422 RSR
bit 3 column ready · bit 4 exception · bit 5 card done · bit 9 fault
423 WCR
← 7 = ready-int + error-int + activate · ← 20₈ clear on fault
A card buffers into 121 words (CTBB), converts through the 1971 CTB1/CTB2 card-code→ASCII tables, gets CR LF appended — a full card errors as 25₈ (NAK) if the process lags.
Notes: Paper tape: reader at 400, punch at 410, single-character DMA-less devices - read data, rearm with 5. Timeouts on the clock level release a stuck reader after 5 seconds. Card reader at 420: status bit 3 column ready, bit 5 tested for end of card, bit 9 for fault; control 7 arms error interrupts too. Card code converts to ASCII through the 1971 CTB tables.

## Slide 21
SECTION 03 · DEVICES · PRINTER
Line Printer IOX 430₈ · driver PNTDR / WPRNT
431 WDR
print character ← A
432 RSR
bit 3 ready for next char · bit 4 error OR (offline, paper out)
433 WCR
← 5 print + interrupt · ← 20₈ device clear, then retry char
% ERROR RECOVERY (WPRNT, N10)
IOX DLP RSR; BSKP ZRO 40 DA
JMP TERR % BIT 4 → ERROR
TERR, SAA 20; IOX DLP WCR
SHA ROT 20; JMP L21 % CLEAR+RETRY
WPRNT substitutes unprintable characters and expands LF handling; output is buffered through 8LP=200₈ words and owned by one terminal via the LPNT lock.
The Versatec option replaces character output with DMA: VERDR fills a 132-char line buffer, loads its address (IOX DLP+1 ), count 1 line ( DLP+3), go (DLP+5 ← 5) — completion interrupts on level 11.
Notes: Line printer at 430. Status bit 3 ready, bit 4 error - the driver clears with 20 octal and retries. Control 5 prints the character in A. WPRNT maps unprintables and pads line feeds. The Versatec variant instead DMA-streams a 132-character line buffer from memory on level 11. Locks serialize it all to one terminal.

## Slide 22
SECTION 03 · DEVICES · DISK
CDC Disk IOX 500₈–507₈ · driver DKTR
500 RCA
read core address
501 LCA
load core address (DMA target)
502 RSECT
read sector counter
503 LBA
load block address — cyl · head · sector packed by DKADR
504 RST
status: bit 2 ready · bit 4 error OR · bit 14 op complete
505 LMR
modus: bits 14–13 op (rd/wr/par/cmp) · bit 2 activate · bit 4 device clear
506 SEEK
position unit
507 LWC
load word count (sectors × 256)
DKTR : X = core addr, T = linear disk addr (256-word sectors), A = op + unit, D = extra sectors (≤3K words). Two retries, then error with the status word in A.
DKADR maps the linear address ÷12 onto cylinders (313 / 626 for CDC 9425 / 9427); unit 1 sits at +52600₈.
The swapper's page ops and the file system's 2K transfers (TRXX) both end here when no drum is fitted.
DISK LAYOUT (FIXED ADDRESSES FROM DKBIT=50₈)
MIB
bitmap
CORL1+2
coreloads
OVDK1/2
overlays
ACCTD
accounts
MAILD
mailbox
USRDK
users
DKA1…DKA12
swap areas
FSYS
file system →
Notes: The CDC disk on channel 500: eight registers. DKTR takes core address in X, NCR-style linear disk address in T, operation plus unit in A, extra sectors in D. DKADR divides by 12 into cylinder geometry for the CDC 9425 or 9427. Status: bit 2 ready, bit 4 error, bit 14 transfer complete. The modus register carries the operation and activate. Below, the fixed disk layout - the drum replaces the front of the swap region.

## Slide 23
04
The Swapping Drum
XDRUM — the NORD-10 drum driver, every register and bit, and the TRSFR front end that routes swap traffic between drum and disk.
“1. APPROXIMATION TO A NORD-10 VERSION” — NJL, 17/4/73
Notes: Section four, the deep dive: the swapping drum. The photo is the actual drum unit under restoration. Nuance: TSS ran on NORD-1s too, but this drum driver is explicitly NORD-10 code - the header calls it a first approximation to a NORD-10 version, and it only assembles when both DRUM and N10 marks are set.

## Slide 24
SECTION 04 · THE DRUM
Drum Basics & Geometry
A drum is a rotating magnetic cylinder with one fixed head per track — no seek arm, no seek time. Latency is rotational only, which made it the swap device of its era.
The controller is a DMA block device : load core address, block address and word count, start it, take an interrupt when done.
TSS ran on the NORD-1 too — but the drum driver itself is NORD-10 code only: pure IOX, guarded by "DRUM N10 , dated 17/4/73.
Sector (block)
64 words
Sectors per track
32
Track = 32 × 64
2,048 w = 1 TSS page
Default size (DRMSZ)
2000₈ × 256 w
= total capacity
256K words · 128 tracks
Notes: Why a drum: one fixed head per track, no seek arm, so latency is rotational only - the ideal swap device. Geometry from the code: 64-word sectors, 32 per track = 2048 words = exactly one TSS page per track. Default DRMSZ 2000 octal 256-word pages = 256K words = 128 tracks. The driver is NORD-10-only: guarded by DRUM N10, pure IOX.

## Slide 25
SECTION 04 · THE DRUM
TRSFR — Drum or Disk?
"DRUM N10 % ONLY WITH BOTH MARKS
TRSFR, STF TRSAV; STX TRSX; ...
TRSF1, LDA TRSAV; SUB (DKA1; SHA 2
COPY DD SA % D = (T-DKA1)*4
SUB (DRMSZ*4; JAN TRSF2% FITS?
LDA TRSAV; SUB (DRMSZ; ...
JPL TRXX% NO → DISK @ T-DRMSZ
TRSF2, LDT TRSAV+1; SHT ZIN SHR 1
SAX 40% 32 BLOCKS = ONE 2K PAGE
JPL XDRUM
JMP TRSF1 % ERROR → RESTART ALL
JMP *-2 % BUSY → CALL AGAIN
TRSF3, ... JMP I TRSVL % FINISHED
D = (T − DKA1) × 4 disk sectors are 256 words, drum blocks 64 — factor 4
First DRMSZ pages of swap → drum. Beyond → CDC disk at T−DRMSZ via TRXX / DKTR.
Op translation: swap ops 1/3 (read/write) shift right → drum functions 0/1. Without the DRUM mark: TRSFR=TRXX — disk only.
Notes: TRSFR is the swap front end. It converts the disk address to a drum block address: subtract DKA1, times 4. Inside the drum: call XDRUM with 32 blocks, one page. Beyond it: fall back to the disk at address minus DRMSZ. Note the busy loop - JMP star minus 2 calls XDRUM again - and the error exit restarts the whole transfer. Without the DRUM mark, TRSFR equals TRXX, pure disk.

## Slide 26
SECTION 04 · THE DRUM
XDRUM — the Programming Interface
% CALLING SEQUENCE
JPL I (XDRUM
JMP ERROR % X=STATUS REG
JMP BUSY % RE-CALL, REGS UNCHANGED
JMP FINIS % X=STATUS, A=CORE ADDR
Busy-exit protocol: call again at once, or after the drum interrupt, with X T A D untouched. The B register is never used.
X
Number of blocks (64-word sectors) to transfer
T
Function — 0 read · 1 write · 2 read test · 3 compare · 20₈ read status only. Bits 8–9 = core-address bits 16–17 (>64K core!)
A
Core address (low 16 bits)
D
Block (drum) address — linear sector number
→X
On error and on finish: the drum status register comes back in X
Notes: The XDRUM software contract, from the header comment. Registers in: X blocks, T function plus core-address extension bits, A core address, D drum block address. Three exits placed right after the call: error, busy, finished. Busy means call again with everything unchanged - the driver is a state machine advancing one hardware operation per call.

## Slide 27
SECTION 04 · THE DRUM
XDRUM — Registers & Bits IOX 540₈+n
540 RCX
read core address (DMA pointer)
541 LCX
load core address
543 LBX
load block address (track · sector)
544 RSX
read status register
545 LCR
load control register (go!)
547 LWX
load word count = blocks × 64
STATUS REGISTER (RSX 544)
bits 4–0
echo of current function code (masked 37₈)
bit 4 DVA=20₈
device active → busy exit
bit 5 ERR=40₈
inclusive OR of errors → error exit
CONTROL REGISTER (LCR 545) — AS ASSEMBLED BY XDRUM
15
14–13 FUNCTION 0–3
12–7 —
6–5 CORE A17–A16
4–3 —
2–0 = 7 INT EN + ACTIVATE
SAA 3; AND DTREG; SHA ZIN 13 % FCN→13-14
LDA (1400; AND DTREG; SHA ZIN SHR 3 % A16/17→5-6
AAA 7; IOX DRM LCR % +INT+ACT → GO
BLOCK ADDRESS (LBX 543) — FROM LINEAR SECTOR NO.
15–11 SECTOR 0–31
10–0 TRACK
The driver splits D into track (D÷32) and sector (D mod 32) with the ROT-13 / ROT-5 shuffle at DRDLC.
Error path: X ← status, then SAA 4; IOX 545 — control ← 4 = device clear by the standard convention [assumed — no controller manual].
Notes: The full hardware programming model at base 540 octal. Six registers via IOX. Status: bit 4 device active, bit 5 error OR, low 5 bits echo the function code. Control word assembled by the driver: function in bits 13-14, core-address extension bits 16-17 mapped to bits 5-6, and 7 in the low bits - enable interrupt plus activate. Word count is blocks times 64. The error path writes 4 to the control register - device clear, by the standard convention, unverified against a controller manual.

## Slide 28
SECTION 04 · THE DRUM · REGISTER DETAIL 1/3
Address & Count Registers 540 · 541 · 543 · 547
541 LCX write
540 RCX reads it back
15–0 · CORE ADDRESS (word address, DMA target/source)
Only 16 bits wide — core-address bits 16–17 go in the control register (next slides). RCX exists for diagnostics; XDRUM never reads it.
547 LWX write
word count
WORDS TO TRANSFER = CHUNK × 64 (64 … 2048)
Driver: SHA ZIN 6 (shift left 6 = ×64). Max one full track: 32 sectors = 2048 words. Whole 64-word sectors only — there is no partial-sector transfer.
543 LBX write
hardware block address
15–11 · SECTOR 0–31
10–0 · TRACK (0–127 on the default drum)
SAD ZIN 13; SHA ROT 13; RADD SA DD % FROM LINEAR D:
SHA ROT 5; SAD 5 % SECTOR=D MOD 32 → 15-11, TRACK=D/32 → 10-0
Notes: Register-by-register, the DMA setup group. LCX takes the 16-bit core address; bits 16 and 17 travel in the control register instead. LWX takes the word count - chunk times 64, maximum 2048 for a full track. LBX takes the packed hardware block address: sector in the top five bits, track below. The driver derives it from the linear sector number D with the rotate sequence shown.

## Slide 29
SECTION 04 · THE DRUM · REGISTER DETAIL 2/3
Status Register 544 RSX · read
15–6 controller-specific — undocumented, returned to caller in X
5 · ERR =40₈
4 · DVA =20₈
3–0 (& 4) FUNCTION ECHO · mask 37₈
bit 4 · DVA
Device active — operation in progress. Driver: BSKP ZRO DVA DA → JMP DBUSY — restore registers, take the busy exit , caller re-calls after the interrupt.
bit 5 · ERR
Inclusive OR of all errors. Driver: BSKP ZRO ERR DA → JMP DERRO — status → X, device clear, error exit . Individual error causes (parity, timing, address) are controller detail — no manual survives.
bits 4–0 echo
Readback of the last function code. Driver: SAA 37; RAND ST DA, then AAA -20; JAZ DRDS1 (was it READ STATUS = 20₈? → finished) and AAA 14; JAP DRILL (> 3 → illegal function, error exit with X = −1).
whole word
Returned in X on both the error and the finished exit — the caller sees exactly what the controller reported.
Notes: The status register, bit by bit, as the driver reads it. Bit 4, octal 20, DVA - device active: the operation is still running, take the busy exit. Bit 5, octal 40, ERR - the inclusive OR of all error conditions; which individual errors feed it is controller detail we lack a manual for. The low five bits echo the function code: XDRUM masks with 37 octal and uses the readback to decide whether it was a status-only call and which function just completed. On both the error and finished exits this whole word is returned to the caller in X.

## Slide 30
SECTION 04 · THE DRUM · REGISTER DETAIL 3/3
Control Register 545 LCR · write = GO
15 —
14–13 FUNCTION
12–7 —
6–5 CORE A17–A16
4 DEV.CLR*
3 —
2 ACTIVATE
1 ERR INT*
0 RDY INT
FUNCTION CODES (BITS 14–13)
0
READ — drum → core (page in)
1
WRITE — core → drum (page out)
2
READ TEST — read & check, no core transfer: surface / parity verify
3
COMPARE — read & compare against core: write verify
20₈
READ STATUS ONLY — software code, never written here: XDRUM answers it from RSX and exits finished
% HOW XDRUM BUILDS THE WORD
SAA 3; AND DTREG % FCN = T & 3
SHA ZIN 13 % → BITS 13-14
LDA (1400; AND DTREG % T BITS 8-9
SHA ZIN SHR 3 % → BITS 5-6 (A16/A17)
RORA ST DA; AAA 7 % + INT EN + ACTIVATE
IOX DRM LCR % GO
Value 7 (bits 0–2) = “enable interrupt and activate” per the source. Value 4 on the error path = device clear / abort. Bits marked * are convention, unconfirmed.
A17–A16 (bits 6–5): extend LCX to 18 bits — DMA into 256K words of core.
Notes: The control register - writing it is what starts the hardware. Bits 13 and 14 carry the function: 0 read, drum to core. 1 write, core to drum. 2 read test - the drum reads and checks but transfers nothing to core, a surface verify. 3 compare - the drum reads and compares against core contents, a write verify. Function 20 octal, read status only, never reaches this register - XDRUM answers it from RSX alone. Bits 5 and 6 extend the core address to 18 bits, 256K words. Bits 0 to 2 are written as 7: enable interrupt, presumably enable error interrupt, and activate. The error path writes plain 4 - assumed device clear. This is the assignment implied by the driver; no controller manual survives to confirm bit 1 and bit 3.

## Slide 31
SECTION 04 · THE DRUM
XDRUM — Transfer Flow & Track Splitting
1
IOX DRM RSX — DVA set → BUSY exit · ERR set → ERROR exit
2
X = 0, or function = 20₈? → read status, FINISHED exit
3
Chunk = min( X, 32 − (D mod 32) ) — never cross a track boundary
4
Load word count (chunk×64), core address, packed block address
5
Advance the saved registers: X−=chunk, D+=chunk, A+=chunk×64
6
Write control word (function + A16/17 + 7) → hardware runs → BUSY exit ; caller re-calls at step 1
ONE 2K-PAGE SWAP = ONE TRACK
32 sectors × 64 w
single operation
unaligned:
tail of track n
head of
track n+1
An unaligned transfer becomes several operations, one busy-exit round trip each.
Interrupt-ready by design: the busy exit lets the caller sleep on the drum interrupt instead of polling — TSS's TRSFR simply polls ( JMP *-2), a “first approximation”.
Notes: The whole driver is one entry point re-called until done. Each call: read status - busy exit if active, error exit if error bit. Done test: X zero or status-only function. Otherwise transfer the next chunk: at most the sectors left in the current track, so a transfer never crosses a track boundary in one operation. Load word count, core address, converted block address, then the control word starts the hardware and the routine takes the busy exit. The caller re-calls; when X reaches zero the finished exit returns status and next core address.

## Slide 32
05
Build, Install, Run
Library marks → FMAC assembly → save to disk → boot a standalone TSS.
Notes: Section five: from source to a running system - configuration marks, the FMAC build, installing on disk, and booting.

## Slide 33
SECTION 05 · BUILD & RUN
Configuration: Library Marks
NCR / CDC
disk system flavor (CDC here)
K12/K14/K16
resident kernel size: 12K / 14K / 16K
DRUM
compile the swapping-drum path (default off)
TEL4…TEL24
number of terminals (4–24)
N10
NORD-10 version : IOX I/O, paging, instruction emulation
DRMSZ
drum size in 256-word pages (default 2000₈)
DEBUG
version B instead of A (separate overlay/coreload areas)
9TTI…9CR
buffer sizes; TT1…TT12, DLP, DCR… device numbers
AS ARCHIVED: CDC MACF DIAB K14 TEL4
→ NORD-1 IOT I/O, disk-only swapping. For the drum system this deck describes: CDC MACF K14 TEL4 DRUM N10
Notes: Configuration is conditional assembly: referencing an undefined symbol on the mark line makes it true. Key marks here. The as-archived builds use CDC MACF DIAB K14 TEL4 - no DRUM, no N10, meaning NORD-1 IOT I/O and disk-only swapping. For a drum-swapping NORD-10 system, add DRUM and N10.

## Slide 34
SECTION 05 · BUILD & RUN
The Build: ASSYSA, Decoded
FMAC % START THE ASSEMBLER
100 / SYSA % PROMPTS: SIZE, NAME
CDC MACF DIAB K14 TEL4 % THE MARK LINE
IOT=160000;ACT=400;... % CVS RESTORATION:
INTDS=150440;... % SYMBOLS MAC HAD BUILT IN
)9ASSM TSS1,LIST1,0 % ASSEMBLE PART 1
)9ASSM TSS2,LIST2,0
)9ASSM TSS3,LIST3,0
)9ASSM TSS4,LIST4,0
)9ASSM TSS5,LIST5,ASYMB:SYMB % + OBJECT STREAM
)LIST % DUMP SYMBOL TABLE
*: / ? / )9TSS % NOT IN ND-60.096 [UNKNOWN]
TSS assembles into memory on the target machine — the overlay machinery even writes overlays to disk during assembly ()WRTM / )SOVER).
The listing streams (LIST1–5) and symbol dumps (ASYMB / BSYMB) in the archive are this script's actual output — a golden oracle : any re-assembly must reproduce those symbol values.
ASSYSB is identical but sets DEBUG, names it SYSB, skips listings → BSYMB.
Notes: ASSYSA decoded line by line. FMAC starts the assembler, the mark line sets configuration, the CVS lines re-define symbols the original MAC had built in. Five 9ASSM commands assemble the parts; the last one writes the object stream and LIST dumps the symbol table. The last three lines are not standard MAC commands - expect to stop after LIST.

## Slide 35
SECTION 05 · BUILD & RUN
Install & Boot
1
MINIT initializes mass storage: MIB bit table, user table, empty file system
2
Run ASSYSA under FMAC — TSS is now assembled in memory, overlays already on disk
3
Execute location 7: LDT *+3; JMP I *+1; SYSSV; CORLD — SYSSV writes 32K words (100₈ × 400₈-word blocks) to the CORLD coreload area, then falls into INIT
4
INIT: interrupt vectors, paging (IPGTB), buffers, links, FINIT file system, enable levels — idle loop waits for a keypress
!
TSS replaces the machine's OS — on an emulator, boot the saved coreload instead of SINTRAN; the master terminal logs on as SINIT when OPR = 131313₈
Notes: Installation: MINIT initializes the mass storage first. Then the assembled system saves itself: executing from location 7 runs SYSSV, which writes 32K words from address 0 to the coreload disk area and jumps to INIT. Booting reverses it: load the coreload, enter INIT - interrupts, paging, buffers, file system - then the idle loop waits for terminals. Remember: this replaces whatever OS was on the machine.

## Slide 36
CLOSING
Open Questions & Next Steps
UNKNOWN
• No MAC / FMAC binary in the archive — the one missing tool
• *: ? )9TSS at the end of ASSYSA — not in ND-60.096.01
• Drum status bits beyond DVA / ERR — controller manual needed
• XDRUM is a self-described “1. approximation” — review before trusting
NEXT STEPS
1 Locate a MAC / FMAC tape image → authentic build under nd100x / RetroCore
2 Failing that: MAC-dialect cross-assembler, verified against ASYMB / BSYMB
3 Build CDC MACF K14 TEL4 DRUM N10 → drum-swapping NORD-10 TSS
4 Exercise XDRUM against the restored drum hardware — carefully
Notes: Honest unknowns and the path forward. The missing tool is a MAC or FMAC binary. The three trailing script lines are undocumented. Drum status bits beyond DVA and ERR need a controller manual. Next steps: emulator plus FMAC, verify against the ASYMB oracle, then bring the drum build up.